## Slide 1
Lane 1 timer &
6 character display
Control box
End gate board
End gate board
LED
LED
Lane 2 timer &
6 character display
Crossed start LED
Crossed start LED
Drag race timer.pptx
RATS PC
End gantry 1
End gantry 2
Start gantry 2
Start gantry 1
LED
LED
Power
Signals
Drag race timer - System block diagram
Start LEDs
Start LEDs
Start gate board
Start gate board

## Slide 2
Gate processor board components & interfaces
5V
Gnd
Beam state
Seen/Not Seen
High when beam broken or not seen
Beam not seen indicator LED and current limiting resistor
= Start crossed indicator
Beam LED and current limiting resistor
Power on LED
switch
Timer /counter board
Beam detector
Sensitivity adjuster
switch
Option to power beam LED from battery when not using gantry
Micro

## Slide 3
Timer /counter board components and interfaces
5V
Gnd
Beam state
Seen/Not Seen
High when beam broken or not seen
Gate sensor board 1
LED driver 1
LED driver 2
LED driver 3
Timer Micro processor
5V
Gnd
Beam state
Seen/Not Seen
High when beam broken or not seen
Gate sensor board 2
Start lights board – This could be incorporated onto the timer/counter board or on a separate board on the end gantry
High - trigger the start light sequence
High - All lights out. start timer
12 V DC supply
or battery
On/off switch
5V reg
Mode selection switches
Control board
Arm/ Start
2 Push buttons
Serial time data
Gnd
5V

## Slide 4
Control board components & interfaces
Timer Counter board 1
Timer Counter board 2
Serial data 1
Serial data 2
Arm/Start 1
Arm/Start 2
Push buttons
RATS PC
USB data link
Micro processor
Gnd
Gnd
Arm/Start 1
5V
5V
5V
LEDS
Mode switches
RATS connected
Timer 1 connected
Timer 2 connected
ARM
START
RESET
OTHER
State display
LEDS
Board gets 5v power from either timer/counter board or the USB cable whichever is connected
From 5v supply inputs